## Slide 1: Anapol : Starting Window
<footer>
<date/time>
Requires an IDL licence (>5.4)

## Slide 2: Anapol : POLDER product selection
<footer>
<date/time>

## Slide 3: Anapol : Area selection
<footer>
<date/time>
Area Selection using the mouse,
…or the numeric fields
The zoom button allows a more precise area selection
The browse button (level 1 product only) produces a browse image of the selected area

## Slide 4: Anapol : Read Product
<footer>
<date/time>
The Output Log window shows information about
the parameters that have been read
=================================== NON-DIRECTIONAL PARAMETERS =========================================
Name Min Max Unit ------ Unvalid ------ ------ Dummy ------ ------ Satur ------
Altitude 36.0 3376.0 meters -35000 0 [ 0.0%] -32767 100 [ 0.6%] 32767 0 [ 0.0%]
Solar Azim. 153.0 190.5 deg. -35000 0 [ 0.0%] 0 100 [ 0.6%] -35000 0 [ 0.0%]
===================================== DIRECTIONAL PARAMETERS ============================================
Name Min Max Unit ------ Unvalid ------ ------ Dummy ------ ------ Satur ------
Sol. Zen Angle 38.2 55.3 deg. -999 0 [ 0.0%] -99 265796 [54.7%] -999 0 [ 0.0%]
View Zen Angle 0.1 70.7 deg. -999 0 [ 0.0%] -99 265796 [54.7%] -999 0 [ 0.0%]
Rel. Azim. Ang 0.0 360.0 deg. -999 0 [ 0.0%] -99 265796 [54.7%] -999 0 [ 0.0%]
Ref_443 -1.9 82.8 % -35000 0 [ 0.0%] -32767 269188 [55.4%] 32767 78 [ 0.0%]
Ref_565 -3.6 58.7 % -35000 0 [ 0.0%] -32767 268779 [55.3%] 32767 1068 [ 0.2%]
Ref_670 -4.1 71.7 % -35000 0 [ 0.0%] -32767 269148 [55.4%] 32767 205 [ 0.0%]
Ref_865 -1.0 72.9 % -35000 0 [ 0.0%] -32767 269884 [55.5%] 32767 303 [ 0.1%]
RefPol_443 -64.0 5.7 % -35000 0 [ 0.0%] -32767 269188 [55.4%] 32767 78 [ 0.0%]
RefPol_670 -59.2 5.7 % -35000 0 [ 0.0%] -32767 269148 [55.4%] 32767 205 [ 0.0%]
RefPol_865 -53.6 5.3 % -35000 0 [ 0.0%] -32767 269884 [55.5%] 32767 303 [ 0.1%]

## Slide 5: Anapol : Data Visualization
<footer>
<date/time>
Parameter Selection
Selection of one particular sequence
Loop through sequences (Directional parameters only)
Overlay geometry angles
View Zenith
Principal Plane
Phase Angle
(Off Glint Angle)
Overlay Map, with high-resolution option (slower)
User defined scaling, or automatic based on 5%-95% of cumulative histogram
Three parameters RGB composites
Visualization resolution
Zoom for details
Scale and Unit

## Slide 6: Anapol : Data Analysis (1/3)
<footer>
<date/time>
A single click in the image generates three windows:
This window shows the physical values of all parameters for the selected pixel
This window opens only for standard “directional” products. It depicts the viewing geometry of successive sequences. Blue lines indicate phase or scattering angle if the corresponding boxes are checked.
This window shows the selected parameter as a function of viewing geometry. The X-axis is either the View Zenith angle, or the phase angle or the off-glint angle. Negative values are used to distinguish ≠ sequences.

## Slide 7: Anapol : Data Analysis (2/3)
<footer>
<date/time>
An area selection (with the mouse) opens two windows
These images can be saved using the File menu
This window depicts the viewing geometry for all selected pixels and their successive sequences. Red box indicates the current sequence.
This window shows the selected parameter as a function of viewing geometry. The X-axis is either the viewing angle or the phase angle or the off-glint angle.

## Slide 8: Anapol : Data Analysis (3/3)
<footer>
<date/time>
If an area is selected and the current parameter is non-directional or no angle is selected, one shows an histogram and a cumulative histogram of the parameter.

## Slide 9: Anapol: Customize parameter list (1/3)
Some POLDER products offer a very large list of parameters, many of them are not useful for most users.

## Slide 10: Anapol: Customize parameter list (2/3)
Select the appropriate product description file in the ANAPOL directory
Comment the lines corresponding to the parameters you are not interested in.

## Slide 11: Anapol: Customize parameter list (3/3)
Parameter droplist shows a reduced set of parameters